Trylon Stamped Drawing Process & Tower Loading Questionnaire

Step 1: Complete all sections of the Trylon Tower Questionnaire*.  Return completed questionnaire to your Trylon Distributor. If you require Distributor contact information, please reach us at info@trylon.com or by fax (519) 669-8912.

Step 2: The Distributor conducts a tower analysis and provides customer with tower model recommendation.

Step 3: To purchase P.E. Stamped Drawings with standard foundation for this tower, customer would place a purchase order with Distributor.

Step 4:   If a P.E. Stamped Drawing is required for a custom designed foundation, a Geotechnical Soils Report should be submitted to the distributor along with the PO.  Any special requirements or instructions should be included.

Step 5: Distributor must ensure that the same questionnaire and soils report/notes (if applicable) accompanies the purchase order to Trylon.

Step 6:  Trylon would then produce the site-specific P.E. stamped drawing. Lead-time for customer to receive drawings is 7 business days after the Distributor places a PO with Trylon. The drawings would be drop-shipped directly to the customer.

Note: Trylon strongly recommends that customer not purchase a tower until they receive confirmation that Trylon has approved the model.

*Note that Trylon accepts no liability for incorrect data supplied by the customer. Therefore, it's incumbent on the customer to do proper research. Any costs resulting from incorrect or missing data will be borne by the customer, including paying for an entirely new P.Eng. Stamped drawing package if it has to be redone with a different tower model.

## DISTRIBUTOR USE ONLY

STANDARD DRAWINGS       (4.77.0101.100, 4.77.0101.200, 4.77.0101.900, 4.77.0101.920)

Customer's completed Tower Questionnaire MUST be submitted at the same time as the PO.

PO MUST reference SuperTitan Tower & Model (i.e. 120' S100... 100' S300... 80' S500... etc.).

Final Tower Model: ___________________________

CUSTOMIZED DRAWINGS     (4.77.0101.302, 4.77.0101.600, 4.77.0101.960, 4.77.0101.990)

Customer's completed Tower Questionnaire MUST be submitted at the same time as the PO.

PO MUST reference SuperTitan KD, SuperTitan MAX or STG Tower & Model (i.e. 120' S100, 194' M310, 180 STG).

Geotechnical Soils Report MUST be submitted at the same time as the PO.

If necessary: Any 'special' information MUST be clearly summarized and submitted at the same time as the PO.

Final Tower Model: ___________________________

TOWER CALCULATION QUESTIONNAIRE FOR TOWERS by TRYLON

Please complete form and submit to your Trylon Distributor. Distributor will conduct a tower analysis and make a tower model recommendation. If you require Distributor contact information, please contact us at info@trylon.com or by fax (519) 669-8912

| Your Name: | Company Name: |
| --- | --- |
| Address: | City: | State: |
| Phone: | Fax: | Email: |
| 1. | Are you currently working with a Distributor for this request? | YES NO If yes, please provide name & contact information: |
|  |  | Company: | Name: |
|  |  | Email: | Phone: |

| 2. | Where will the tower be installed? | County: | Site Address: | City: |
| --- | --- | --- | --- | --- |
|  |  | State: | Latitude: | Longitude: |

| 3. | What is tower height? (Select one) | Feet | Meters |
| --- | --- | --- | --- |

| 4. | Structure Type: (Select one) | Self Support (SS) Guyed Bracketed Other |
| --- | --- | --- |

| 5. | What type of Trylon tower? (Select one) | SuperTitan KD SS (up to 190’) SuperTitan Weld SS (up to 150’) SuperTitan MAX SS (99’ to 251’) STG Guyed (up to 480’) Titan SS (up to 96’) Note: Titan towers cannot be stamped by a P.Eng |
| --- | --- | --- |

| 6. | Which definition of wind speed do you wish to base the tower analysis? (Select one). Following are definitions: Survival: max. Sustained wind gust recorded over past 30-40 yr period. Cannot be used if Engineer’s stamp is required. EIA-222-F: (USA only) = basic county wind speed defined by EIA standard. Specified in some areas. TIA-222-G: (USA only) = Most recent revision of US testing standard = basic country wind speed defined by TIA standard CSA: (Canada only): wind pressure defined by CSA S37 standard. Cannot be used for the Titan tower | Survival EIA-222-F (in USA) TIA-222-G (in USA) (if TIA-222-G is selected, please complete Pg. 3) CSA S37 (in CAN) |
| --- | --- | --- |

| 7. | What is the maximum wind speed, as dictated by the wind speed definition in (6) above. (May be obtained by contacting your local weather office, other weather service, or local building permit office.) |  | MPH of wind speed |
| --- | --- | --- | --- |
|  |  | or |
|  |  |  | PASCALS of wind pressure |

| 8. | Will any radial ice accumulation occur? (May be obtained by contacting local weather office, other weather service, or local building permit office.) | Yes | If yes, how thick: |
| --- | --- | --- | --- |
|  |  | No | inches | mm |

| 9. | Is an Engineer’s stamp required on the tower drawing? Contact your local building code authority or permit office to determine if this is required. (Note: if so, a more expensive tower may be required This is a 1-page drawing that shows the sections of the tower being stamped from the foundation section to the top. It also states in chart form the exact antennas being installed, the exact transmission lines being installed, the wind speed and ice loading at the site and the national standard for which compliance is being wet-stamped by an engineer. In addition a report showing the capacity of tower members is also included. This drawing does NOT provide customer-specific details such as antenna mounting illustrations, grounding details, or other non-standard items.) | Yes No |
| --- | --- | --- |

| 10. | Is an Engineer’s stamp required on foundation drawing? Contact your local building code authority or permit office to determine if this is required. (Note: if so, a more expensive tower may be required. If answer is yes, and the soil conditions are other than ‘Normal Dry Soil’, then Trylon will require a Geotechnical Soils Report taken at the site where the tower will be installed. If the customer provides no geotechnical soils report, then Trylon must assume Normal Dry Soil and the customer must bear the full risk of that assumption being incorrect. To mitigate customer risk, Trylon highly recommends that customers hire a 3rd party geotechnical consultant to conduct a geotechnical soils report. If required, a foundation drawing wet-stamped by a professional engineer may be purchased from your Trylon Dealer at an additional fee. This foundation drawing provides only: excavation details, concrete details, quantity and size of rebar, reactions at the base, overturning moment. It does NOT include seismic analysis, detailed rebar drawings or other non-standard foundation requirements. Consult Trylon if your drawing requires special information at an additional fee.) | Yes No |
| --- | --- | --- |

| 11. | Antenna Information: |
| --- | --- |

| Antenna# | *Elevation Of Antenna (Feet) | **Offset Distance (feet) | Antenna Manufacturer Model Number/Type: (Dish, Yagi, Omni Dipole, Other) | L x W x D of Antenna | ***Flat or Round | Projected Surface Area (sq. feet) | Weight (lbs) | Transmission Lines |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | Qty | Size (inches) |
| 1 |  |  |  |  |  |  |  |  |  |
| 2 |  |  |  |  |  |  |  |  |  |
| 3 |  |  |  |  |  |  |  |  |  |
| 4 |  |  |  |  |  |  |  |  |  |
| 5 |  |  |  |  |  |  |  |  |  |
| 6 |  |  |  |  |  |  |  |  |  |

| 12. | Optional Accessories: (Check all that apply) | Fall Protection Step Bolts Anti-Climb Grounding Kit Lightning Rod Antenna Mounts Other: |
| --- | --- | --- |

| 13. | Structure Information: what type of application is the tower being used for? (Check all that apply) | Broadband Microwave HOP GPS Private Network Scada Wireless LAN Lighting Other: |
| --- | --- | --- |
| 14. | Additional Information: Comments or Special Requirements: |  |
| Note: Page 3 only needs to be completed if TIA-222-G was selected. |
| 15. | Importance Class: | Importance Class 1: ie: Structures used for services where a delay in returning the services would be acceptable such as residential wireless, conventional two-way radio, television, scanner reception, wireless cable, amateur and CB radio. Importance Class 2: ie: Structures used for commercial services such as commercial wireless, television and radio broadcasting, cellular, PCS, CATV operators and microwave communications. Importance Class 3: ie: Structures used for essential wireless communications such as civil or national defense, emergency rescue or disaster operations, military navigation where a delay in the services would be unacceptable. NOTE: If section is not completed the tower analysis will default to Class 2 |
| Questions 16-18 only need to be completed if Class 2 or 3 was selected. |
| 16. | Exposure Category: | B: (Urban, fully built-up area) C: (Rural open terrain – default and most common exposure category) D: (Within a half mile of a shore line NOTE: If section is not completed the tower analysis will default to Category C |
| 17. | Topographic Category | 1: (No abrupt topographic changes immediately surrounding the tower) 2: (Tower located, within a distance equal to the height of the tower, on or near the crest of an escarpment) NOTE: If section is not completed the tower analysis will default to Category 1 |
| 18. | Site Class: Required where earthquake loading is to be investigated. This information maybe obtained from the US Geological Survey | A: (Hard rock with 10-ft or less of overburden) B: (Competent rock with moderate fracturing with 10-ft or less of over burden) C: (Very dense soil, soft rock or highly weathered and fractured rock) D: (Stiff Soil) E: (Weak Soil with high moisture content) NOTE: If section is not completed the tower analysis will default to Class D |

# Text boxes

**Offset distance is from the centroid of the tower to the antenna’s center of mass.

*

***

# For additional information, check out our website

www.trylon.com